## Slide 1
Experimental Investigation and Analytical Modeling of Unsteady Vortex Flows
Dr. Juhi Chowdhury
Department of Mechanical and Aerospace Engineering
University at Buffalo

## Slide 2
Unsteady Vortex Flows
Aircraft Wing
Drone
MAV (Micro Air vehicle)
Bio propulsion
Notes: Why is the research in unsteady vortex flows important? This type of flow is seen in abundance in the nature. One example is fish swimming. An understanding of the vortical structures and vortex breakdown is essential for the development of air vehicles of different scales and maneuvering capabilities.

## Slide 3
Rescue mission
Agriculture
Drones
&
MAVs
Deliveries
Research
Photography
Military
Desirable feature: Maneuverability
Application Area: Drones & MAVs
Military
MAV: Micro Air Vehicle
Black hawk from Praxodynamics
Notes: What are drones useful for?

## Slide 4
Drones/UAVs in gusts
Disturbance intensity can be on order of UAV speed; most relevant gust width is size of wing chord.
UAVs must be highly agile and able to handle gusts.
Gusts in atmospheric boundary layer (ABL)
Jones, Cetiner, Smith Ann Rev. Fluid Mech. 2021
Notes: Fixed wings air vehicles have limited capability in this kind of extreme weather conditions.
like gust, the wings may have to have complex motions or shape change.
For that, we can take inspiration from the nature…

## Slide 5
Motivation & Objective
Inspiration
from
nature
Ward-Smith 1984
Hubel et al, 2009
Purdue University
Notes: In case of various flying animals, such as, birds, bats, insects.
Their wings rotate, translate, pitch, fold, twist, bend…so many sophisticated features they showcase!

## Slide 6
Motivation & Objective
Inspiration
from
nature
α
chord
Ward-Smith 1984
Rotating tip panel with aft sweep
Rectangular main wing
chord
span
Umain
Taira & Colonius, JFM ’09
Carr et al., JFM ’15
Taira & Colonius,
JFM ’09
LEV
TV
TV
Translation, rotation, & sweep
Gust mitigation technique: varying wingtip geometry of a translating wing— rotating panel with aft sweep
Periodic LEV shedding
Periodic lift changes
Attached LEV
Sustained lift
Attached LEV
Sustained lift
Notes: ->An important aerodynamic feature of this flight is flow separation due to high angle of attack. Here The flow separated and rolled up into a leading-edge vortex
that generates high lift but then sheds. But for small AR rotating wings, LEV stays attached, giving a sustained lift. If there is a sweep,
that promotes spanwise flow helping with LEV attachment .
Therefore by combining sweep and rotation, we can expect to change the vortex dynamics to our advantage in wing translation.
Our goal is to mitigate the gust effect by rotating a tip panel which also has a sweep and also learn how the vortex dynamics changes
.

## Slide 7
Force measurement
Qualitative flow viz.
Quantitative flow study
Modeling
Research techniques
Notes: I measured lift to study the effect of gust and gust recovery performance.
I used dye-flow visualization to study the flow qualitatively , then used 4D PTV to acquire in-depth knowledge of the vortex dominated flow to justify the lift variations.
Finally, a low order modeling will bring a nice closure to the study.
Since modeling this particular wing flow would be difficult, there is translation and rotation involved. I focused on a small part for modeling..that is the rotational component of the wing

## Slide 8
Objective: develop a 3D analytical model for unsteady rotating wings and compare it with available experimental and numerical results.
Application: mathematical models used for vehicle design, such as drones, and flight controller.
Model for the Unsteady Lift of Rotating Wings
Chowdhury, J., & Ringuette, M. (2019). A simple vortex-loop-based model for unsteady rotating wings. Journal of Fluid Mechanics, 880, 1020-1035
Notes: Since our group performed experiments on rotating wings in the past, I already had data available to work on a model and compare against those data.
This type of modeling is important for aerodynamic and control system design for bio-inspired drones.
But such efforts have often been limited to being two-dimensional, semi-empirical, sometimes computationally expensive, or quasi-steady.
The current model is unsteady and three-dimensional, yet simple to implement.

## Slide 9
Wing schematic & 3D vortex loop
Model Assumptions
AR=2 exp. from Carr et al. (2015)
AR=4 simulation from Jardin & Colonius (2018)
Growing vortex loop
b = span
c = chord
RV
TEV
LEV
TV
Loop is tilted
The model assumes a coherent planar vortex loop structure: LEV-TV-TEV-RV
Notes: Rotating wings produce a vortex loop consisting of
-> the root vortex, -> leading-edge vortex, -> trailing-edge vortex, and –> tip vortex.
The trailing edge vortex remains where the motion starts.
The leading edge vortex stays attached to the wing.
The loop grows as the rotation angle increases,
therefore also in time.
->This is modelled as a tilted planar loop,
geometrically specified by the wing size, orientation and motion.
What I mean by orientation is that the loop has an angle theta
w.r.t the horizontal plane, -> which is different from the angle of attack.
In reality, the rotating wing flow is very complex and 3D.
There are a lot of details in the structures,
but we take advantage of the coherent loop structure and simplify the problem.

## Slide 10
Basic Framework
Circulatory
Inertial Lift:
(Potential flow, blade element: Percin & van Oudheusden, 2015)
Total lift:
: Angular acceleration of the wing
α: Angle-of-attack
: wing span
: wing chord
: span + root distance
: fluid density
Inertial
: Loop circulation
: Vector area spanned by the loop
: Projection of onto the horizontal plane.
Notes: -> There are two main contributions to the lift force on the wing:
->inertial lift… which is present during the wing acceleration. When the wing accelerates, it accelerates the fluid surrounding it.
-> That accelerating fluid gives force to the wing which is called the inertial force. Inertial lift can be calculated simply using potential flow theory. It includes wing kinematic and geometric parameters that are known to us already.
-> 2nd contribution to the lift is the vortex force or circulatory force. Modeling circulatory force is challenging.
To find circulatory force, I need -> the loop circulation,
and loop area on the horizontal plane,
which is given by -> this formula. Phi is angle of rotation.

## Slide 11
Basic Framework
: Loop circulation
: Vector area spanned by the loop
: Projection of onto the vertical plane.
Impulse of thin vortex loop:
Circulatory
Total lift:
Sullivan et al. (2008) showed that the momentum of the volume of fluid displaced by a piston is approximately equal to the impulse of vortex ring.
Angular momentum of the volume of fluid displaced by the motion of the wing.
Angular impulse of the vortex loop about the axis of rotation.
Running mean of rotational speed:
Radius of gyration:
Approximate fluid mass displaced by the wing:
Notes: Sullivan et al. showed that …the momentum of the volume of fluid displaced by a piston ….
is approximately equal ….
to the impulse of the vortex ring generated by the piston motion.
The impulse of a thin -> 3D vortex loop can be found from this relation.
Drawing an analogy to the rotating wing-flow ->…..
I equated the -> angular momentum of the volume of fluid
displaced by the motion of the wing….
-> to the angular impulse of the vortex loop….about the axis of rotation.
Definition of each symbol is given on the right.
Two things are unknown in the momentum balance equation:
-> the loop circulation and ->the loop area
-> projected onto the vertical plane.

## Slide 12
b
Schematic of loop on the horizontal plane
Basic Framework
Notes: ->From the planar loop geometry, S vertical -> can be expressed as this.
Once S_vertical is ->substituted in the momentum balance,
we get a -> simplified form for the loop circulation.
So essentially it becomes a problem of finding the loop angle, theta.

## Slide 13
Finding Loop-angle θ
Biot-Savart Law:
Induced angle:
Downwash
&
Total lift:
α scaled by near-wake flow:
Modified angle-of-attack
Induced angle
Notes: Finding the loop angle was challenging as the loop structure is very much three dimensional.
In the interest of time, I will skip the details. But..briefly…
I used the concept of ->
modified angle of attack by the near wake flow ….
-> and downwash,
-> to find tan theta.
Everything in this term is known from either geometry or kinematics.
Therefore -> plugging all these, lift can be found.

## Slide 14
Unsteady lift comparisons
----- Model
Experiment/simulation
AR 2
α
AR = 4, 3, 2
α
AR 2
α
Within 18% deviation during wing’s steady motion.
Motion Profiles
Good trend match.
Within 20% deviation for mean lift, for some cases, below 10%.
Notes: I took a variety of cases from different research groups to compare my model with…
for example, UB2 3 4 are the experimental results from our group.
The others are: TU Delft, UMD, RVC, and AFRL.
->They have different ARs, Reynolds numbers, root cutouts,
-> and accelerations.
In the motion profiles, you can see that the wing at first accelerates
over certain rotation angles,
then rotates at a constant angular velocity.
For the force plots, X axis is angle of rotation….
that is representative of time,
and y axis is lift co-efficient.
In general the lift trend has a peak due to acceleration,
and then over time saturates.
There is -> overall good agreement.
->The model reasonably predicts lift co-efficient ….
within 18% of the experimental results during the wing’s steady motion.
And the trend is also captured well.
It is not always effective at capturing -> the startup-acceleration peak,
and the deviation is more than 20% of the experimental results.
However, -> it gives a reasonable estimate of the peak
when compared with the numerical simulation.
For mean lift, -> the deviation is within 20%,
for some cases it is below 10%.

## Slide 15
Steady lift comparisons
from the unsteady model averaged over Ф
Steady-state form of the model:
Excellent agreement with the experiment over a range of angles-of-attack
Notes: Dickinson et al. measured the steady lift for a robotic fruit-fly wing …..rotating from rest ….for angles of attack ranging from 0 to 90.
I used a rectangular geometry, but matched the wing area and Rossby number for my model.
I compared two things with Dickinson’s experimental results:
I mathematically derived a stead-state equation …from the unsteady model I talked about earlier….solid line shows the steady state model. And also the formula is very simple.
I took another approach: I averaged the CL from the unsteady model… over 150 degrees to 250 degrees of rotation angle. It’s shown with asterisk symbol on the plot.
The both approaches have an excellent match with the experimental data.

## Slide 16
Wings experiencing gusts
U
t
Greenblatt et al., 2016
U
U
t
t
Chowdhury & Ringuette, 2020
Longitudinal/Streamwise gust
Vortex gust
U
Zaloglu et al., 2020
Gust velocity, V
Andreu-Angulo et al., 2020
Transverse gust
Notes: researchers have been looking into various kinds of gust responses… in attached or separated flows.
For transverse gust, the gust velocity acts perpendicular to the wing velocity.
Two types of velocity functions: a square wave function , and a sine wave variation.
A wing can also experience vortex gusts.
I looked into streamwise gusts where gust velocity acts along the wing velocity: we are using step velocity functions….
another group is looking into periodic streamwise gusts.

## Slide 17
Execute streamwise step-up and step-down gusts in water towing tank at 21c traveled.
Approach
Step-up gust
Step-down gust
U
U
Re=6K
Re=9K
Re=10K
Re=5K
Gust:
amplitude = 0.5Umain,initial
width = 1c
Notes: Streamwise gust means there is a sudden increase or decrease in velocity in the streamwise direction.
For our case, we increase the speed by 50% for stepup and decrease the same amount for stepdown, over 1 chord distance during wing’s travel.
The gust starts at 21 chords distance from the start of the wing motion.

## Slide 18
Wing model
DC motor for tip motion
Control rod
c
Λ
Umain
Upanel
𝛬
AR = 4, with panel: 6
= 45 (extended)
Upanel = 1.5Umain,initial
Execute streamwise step-up and step-down gusts in water towing tank at 21c traveled.
chord
= 45
Approach
U
Actuation-in,
Staticsweep -> rectangular
Actuation-out,
Rectangular -> staticsweep
U
Step-up gust
Step-down gust
U
U
Re=6K
Re=9K
Re=10K
Re=5K
Gust:
amplitude = 0.5Umain,initial
width = 1c
Parameters
*Chowdhury, J. & Ringuette, J. M., AIAA J, 2021
Notes: For step-up gust, the wing starts out with the panel extended..calling that “static sweep” , then after actuating the tip inward it becomes a rectangular shape.
The opposite is true for stepdown. Starts out as a rectangular wing, then after actuating the tip outward, becomes staticsweep.
I use AR 4 for rectangular shape, 6 with the panel extended. Angle of attack 45 deg., sweep angle 45 when extended.

## Slide 19
Experimental setup: towing tank and wing
Towing tank (not filled)
4m x 1.5m x 1.1m glass-walled water towing tank, 3m H2W linear stage.
Linear motor
Wing
Planform view
DC motor for tip motion
Motor arm
Control rod
Rotating tip panel
Pivot
Rect. main wing
b
c
Λ
Umain
Upanel
𝛬
~1/8-circle tip panel rotates via a pivot, fully-retractable inside wing.
Panel driven by DC servomotor + arm, via control rod through inside of wing.
ATI Gamma transducer is used for force measurements.
Notes: Here’s the experimental facility.
->We installed a 3m long linear stage on this glass water tank.
->The wing is suspended vertically from the linear stage.
->The rectangular flat plate wing has a tip panel attached via pivot at the wing tip.
That panel can be rotated in and out of the wing…
-> using a control rod that goes through the inside of the wing. The other end of it is attached to a motor arm.
This motor and the linear stage work in sync with the help of a programmable controller.
For force measurement, a transducer is attached at the base of the wing.

## Slide 20
Neutrally buoyant dye through gravity-feed system.
Dye ports: along LE, at TE corner (internal); along tip aft of pivot (external).
3 orthogonal HD cameras; white lighting against white backgrounds.
Experimental setup: dye visualization
Not to scale
Aft-view camera
Top-view camera
End-view camera
Notes: For dye viz experiments, white backgrounds are added and the wing is painted white for better contrast.
3 dye tubes are internally embedded and one is externally attached. These tubes feed dye to the points of interest.
The neutrally buoyant dye is prepared in-house.
The dye is delivered through the gravity feed system.
3 orthogonal camera views were captured to have a better visualization of the flow.

## Slide 21
*Not to scale
Dual-head laser
Wing
Tow direction
X
Z
Y
4D PTV: “shake-the-box” (STB)
  Fluorescent particles, 100 m
  Photonics dual-head Nd:YLF laser
  4 high-speed 4MP CMOS cameras
  Recording: 155 Hz during step-up; 66 Hz step-down
3 streamwise-shifted volumes stitched; 5 realizations merged
Lagrangian to Eulerian velocity: “binning”—Gaussian-weighted avg. of PTV
Experimental setup: Particle Tracking Velocimetry
Notes: For PTV experiment, 4 high speed 4MP cameras are arranged in a linear fashion.
A dual head laser is used for illuminating the measurement volume
100 microns fluorescent particles were chosen as tracer particles.
For stepup gust, the camera records at 155 Hz, and for stepdown, at 66 Hz.
For limitations regarding the camera arrangement and spatial resolution, at a time only a certain measurement volume size could be used. But I staggered the wing start position to cover larger portion of the wing path.
In this video you are seeing particle tracks. I was blown away when I saw this for the first time. To be able to visualize real vortices like this is amazing!
From PTV, we get lagrangian velocity, that is then converted to Eulerian velocity.

## Slide 22
Step-down gusts
Step-up gusts
Gust start
1c ends
3c ends
6c ends
Effect of Gusts on a Rectangular wing
LEV
TV
TEV
shed LEV
TV
TEV
new LEV
End view
Top view
End view
Top view
No-gust
No-gust
Notes: For both gust types, step up and step down, I changed velocity ramps to explore, only for force measurements though:
Red 1c, green 3c, blue 6c
For step-up gust, the lift co-efficient increases dramatically and for step-down, it decreases significantly.
You can see the changes in lift when compared with the no-gust level- the dashed curves.
Compare the red curve with the green and blue curves: the lift changes are higher for higher acceleration or deceleration due to gusts. The effects persist even after the gust ends.
Step-up 1c ramp shows 2 distinct circ.-force peaks. The 2nd peak is present for 3c ramp but not for 6c.
Those circulatory lift peaks are due to the formation of LEVs. When the LEV sheds there’s a drop in lift.
The drop in lift for Step-down is due to the prior wake impingement and interaction with the wing. Impinging wake disrupts the tip vortex flow.
Notice how the wake for stepdown looks different from the stepup case. The wake is wider in the span and chordwise direction.
The LE shear layer is deflected upward. The overall wake angle increases dramatically, which could explain the lift force drop.
But finally the CL recovers to a circ. peak for all cases.

## Slide 23
1c ramp
3c ramp
6c ramp
AR=4
AR=2
Early 21.5c actuation lowers gust peak, 50% ramp actuation more sustained
Greater effect vs. AR = 4
CL uses instantaneous Umain(t) & time-varying wing area
Effect greater for AR = 2, larger relative panel area
Tip actuation-in reduces lift increase due to step-up gust
Shape change: Static sweep to Rectangular
Notes: The tip is actuated inward for the step-up gust. Before actuation, the wing is a static sweep configuration, after actuation, it becomes rectangular.
Lift co-efficient is calculated using instantaneous velocity and time varying wing area.
Earlier we saw that due to the step-up gust, the lift co-efficient increases, this amount of increase varies with gust ramp distances and also aspect ratios.
So our aim is to bring the lift co-efficient down, closer to the no-gust CL level.
Two reference static shapes : rectangular and staticsweep, are taken for comparisons
-> 21.5c actuation lowers lift in the first vortex dominated peak,
“point 1c added mass” this is added mass dominated peak, the actuation doesn’t have any effect on that.
AR2 shows more pronounced effect for actuation, than AR4, because of the larger panel area change w.r.t the main wing area
->When the tip is actuated at 50% gust ramp, the actuation has more prolonged benefit.
For 1c ramp, 21.5c actuation is the 50% ramp actuation.
To put things into perspective, an air vehicle will experience lower lift as the wing area is reduced. In these charts, that effect is not included. The changes you see here is coming from purely vortex dynamics changes. In reality, the net effect will be greater than what you see in these charts.

## Slide 24
Rectangular
Static sweep
Actuation-in
Step-up gust

## Slide 25
Calculate total circulation of LEV-signed vorticity in 1c x 1c “box” following wing.
Total circulation in chordwise (const.-span) planes
0.75b
b = span
b
Rectangular step-up gust
Notes: To study the differences in flowfield for the two types of gusts and also variation in wing shapes, I focused on total positive circulation near the wing.
It is calculated using the positive spanwise vorticity, omega_z in the 1c by 1c square region as indicated by the black box using that formula. The positive ωz is contained in the LEV and the negative in the TEV.
The plot on the right hand side shows total positive circulation calculated in the box, vs chords distance traveled by the wing.
The box moves with the wing as it translates. Essentially, the box contains all LEVs that are close to the wing, and are likely to contribute to the lift force on the wing.

## Slide 26
Total circulation for step-up gust
0.65b
0.75b
0.90b
1.05b
b = span
b
65% span
105% span
75% span
90% span
Notes: I compared 21.5c actuation-in with the rectangular and staticsweep cases for step-up gust in terms of total positive circulation near the wing.
Since this is a planar treatment, different spanwise locations are chosen: we have 65%, 75%, 90%, and 105%.
Overall the total circulation on the wing increases and then decreases. A similar pattern is observed in lift between 21 and 26 chords traveled.
the static sweep (gray curve) is higher than rectangular case in some parts of the wing travel after the gust.
Before actuation, that is before 21.5c traveled, , all 3 cases are similar, except for 105% span. Then actuation-in (red curve) eventually drops to the rectangular level (the black curve), and in some cases even lower than the rectangular wing, ….especially for 65% span, even though the wing attained the same rectangular shape after the actuation.
These effects are reflected in the lift-coefficient.
Another thing to notice is the the total circulation for actuation-in case starts to deviate from that of the static sweep earlier outboard, such as at 105% span, later inboard as expected.

## Slide 27
6c ramp
3c ramp
1c ramp
Sustained from actuation above swept, similar to rect.
Sustained from actuation
Relatively larger actuation peaks
21.5c act. peaks like AR = 4 case (new AR is 4.1); swept lower
Faster recovery
Actuation out: attached swept-edge vortex (SEV)
AR=2
AR=4
Tip actuation-out reduces lift decrease due to step-down gust
CL uses instantaneous Umain(t) & time-varying wing area
Shape change: Rectangular to Static Sweep
Notes: Stepdown gust is basically slowing down. Therefore, we observed that the wing loses lift depending on the gust ramps.
For the gust mitigation purpose, we have to produce more lift to overcome the the lift loss.
So the tip is rotated outward during the gust.
->And we do achieve lift boost by doing so…as you can see the red curves are higher than the rectangular and static sweep cases overall.
21.5c actuation seems a bit too early for 3c and 6c ramps to alter the gust force.
-> Tip actuation outward at 50% gust ramp also reduces the lift drop significantly for all cases.
Actuation is more effective in mitigating gust for AR=2 …as expected because of greater planform change.
For the actuation out case, post-actuation CL is closer to that of the rectangular wing than the static sweep case although its post actuation shape is same as the static sweep.

## Slide 28
Rectangular
Static sweep
Step-down gust
Actuation-out

## Slide 29
65% span
75% span
105% span
130% span
115% span
90% span
Total circulation for step-down gust
Rectangular case,
Notes: For stepdown gust, the total circulation decreases with chords travel.
It could be partly because the vortices are leaving the box where I calculate the total circulation as you can see in this movie.
Due to slowing down, the LEVs rapidly shed.
For 115% and 130% span, the red curve goes up that is because, the tip panel has been actuated out, so there’s a new surface where new vorticities will be created. That definitely helps this case to overcome some lift loss.
Also, overall, in places, the red curve is higher than both the rectangular and static sweep cases, especially for inboard locations.
->Which explains why the lift coefficient is higher and more sustained.
Before actuation-out, the total circulation for the actuation out is similar to that of the rectangular case since they had the same shapes. But after actuation, though the wing shape resembles static sweep case, the total circulation is somewhat higher than that.
In stepup, you saw the static sweep was higher than rectangular. Here during some portions of the travel, it is opposite. That also is consistent with the fact that CL is lower for the static sweep.

## Slide 30
Takeaways
Inward tip actuation can mitigate the gust-impulse change by as much as 38% and outward tip actuation by 84%. Effects are present even when wing area & velocity changes accounted for.
Actuation-in reduces over much of span—coincides with lower .
For actuation-out, is sustained above static cases across much of the span—coincides with higher plateau before all cases recover.
In most cases, actuation yields better gust-force change for AR=2 than 4, due to the greater change in wing planform.
Actuation timing and ramp distances also play a role.
Chowdhury, J. and Ringuette, J. M., “Effect of a Rotating and Swept Wingtip on Streamwise Gust Alleviation”, AIAA J, 2021
Acknowledgments
National Science Foundation (Award # CBET-1706453) supervised by Dr. Ronald Joslin, and award no. CBET-1828544 (MRI Program), supervised by Dr. Shahab Shojaei-Zadeh.
Prof. Matthew Ringuette, Karan Shah, Adam Hammond.

## Slide 31
Fluid-Structure Interactions in Face Masks
Center for Fluid Mechanics
Brown University
Collaborators: Kenny Breuer, Rajat Mittal, Kourosh Shoele, Erin Tucker, Jay-Young Cho
Notes: As part of my post-doctoral research with Kenny Breuer at Brown University, I worked on fluid structure interactions in face masks.

## Slide 32: Motivation & Objective
Background
Face masks reduce the spread of airborne diseases
Lack of understanding of fundamental material and mechanical properties of masks
Goal of the Study
Air permeability over a range of flow rates
Mechanical deformation of masks due to pressure drop
Notes: Face masks were invented to stop the spread of airborne diseases and have been very effective in curtailing the transmission of the COVID-19 virus.
In the year 2020 alone, extensive research has been published, specifically on filtration efficiency of mask materials,
Another important factor to consider while manufacturing masks is breathability.
In that context, I calculated air permeability over a range of flow velocities of different mask materials and observing the relationship between mechanical deformation and pressure drop.
These would provide a fundamental basis for understanding fluid structure interactions of face masks.

## Slide 33: Schematic of the Experimental Setup
Mask material deflection
Mask Material
Airflow
h
R
Laser Beam
Needle Valve
Flowmeter
Pressurized air
from the wall
Air Chamber
Pressure Transducer
Laser Displacement Sensor
3D Printed Ring
Mask
Material
Airflow
Pressure Regulator
Parameters | 
Temperature | 20 – 25 °C
Relative Humidity | 30 – 60 %
Flow rate | 0 – 100 SLPM
Differential pressure (across mask) | 0 – 600 Pa
Notes: The pressurized air enters the system and passes through a
pressure regulator, a needle valve, the primary tool for velocity control, and a flowmeter. It finally
enters the air chamber. At the top of the box, there is a small 3D printed ring, on top of which the
mask material is clamped. The differential pressure transducer measures the pressure
difference across the mask material while the laser distance sensor measures the displacement
at the center of the material.
The flow rates were chosen based on physiological data.

## Slide 34: Darcy’s Law for airflow through masks
For Re < 10 :
For Re > 10, the inertial term (Forchheimer term) is added.
Material thickness is very small. The final form:
 | Pressure change across the mask/fabric thickness
 | Airflow velocity
 | Permeability of the medium
 | Inertial permeability of the medium
 | Pressure change across the mask/fabric thickness
 | Airflow velocity
 | Permeability of the medium
 | Inertial permeability of the medium
Notes: I calculated permeability using Darcy’s Law, which correlates pressure difference with
velocity. The pressure gradient has two contributions: one is viscous, linear, and another is
inertial, nonlinear. For a low Reynolds number, the linear term dominates.
Permeability is represented by k, scaled by thickness, it’s k’ .

## Slide 35
Aydin et al., Extreme Mechanics Letters, 2020.
Rengasamy et al., Ann. Occup. Hyg., 2010.
Zangmeister et al., ACS Nano, 2020
Comparison with available research data
: | Permeability of the material
 | Permeability of the material
*All data are for a single layer material.
Notes: Here in this chart, you are seeing different kinds of mask materials on the x axis and their logarithm of permeability on the y axis. Different colors indicate data from different groups. Multiple circles of the same color and the same material indicates different samples.
Permeability of medical masks, N95, and KF94 are comparable and also are lower than that of cotton, polyester, silk, and chiffon. While our results are
Comparable with the other groups, our values tend to be a bit higher than the rest, especially for more permeable
Materials. This may be due to the larger presence of nonlinear
permeability that is not accounted for in the literature.

## Slide 36
Permeability of multiple fabric layers
: permeability of layers of mask material with thickness ignored
Various symbols represent different samples of the same mask/fabric type from the same manufacturer.
Notes: We investigated permeability in multi-layer mask. You can see as one adds more layers, the pressure drop increases for the same velocity, therefore, permeability decreases. I found that the permeability showcases a hyperbolic nature with the number of layers as shown by this relation. When tried for all different materials, the normalized permeability does collapse at value 1. It was very interesting to be able to find a parallel resistor connection type relation.
This is a very prominent finding in the context of mask manufacturing.

## Slide 37
Mask material deflection under pressure
[1] Eaton et al., MSM 99
Airflow
h
R
: Maximum deflection
: Elastic modulus
: Poisson’s ratio
: Initial strain
: Thickness
Small membrane deflection [1] (h < t/5)
Large membrane deflection1 (t/5 < h <3t)
  .
,
High thread count cotton
h : Deflection
R : radius
Stiffness constant,
 | layers
Black | 1
Red | 2
Notes: we also explored mechanical deformations of mask materials. The
material bulges out like a spherical cap and we measured the deformation at the center under
different levels of pressure drop.
The deflection ‘h’ increases with an increase in pressure drop and the single
layer shows more nonlinearity and higher deflections than the double layer case. Theories for fabrics are rather complicated and we opted for a thin plate theory to describe the
mechanical behavior.
For small deflection, deformation “h” has a linear relation with pressure drop, and for
a larger deflection, it has a cubic root relation.
I calculated psi inverse, which is equivalent to a linear stiffness constant
involving Young’s Modulus. Except for cotton, psi increases with the number of layers.
Overall, medical masks, N95, and KF94 have higher stiffness than the other fabrics,

## Slide 38: Summary
Analyzed permeability coefficients under a range of flow velocities
Found a hyperbolic relationship of permeability to the number of layers for various kinds of mask materials
Investigated structural property related to elastic modulus from the variation of mask material deflection with pressure change
Acknowledgments
Thanks to the sponsor, National Science Foundation, and Ben Lyons (Brown University), Prof. Kourosh Shoele (FSU) and Prof. Rajat Mittal (JHU)
Notes: To conclude, I analyzed permeability of different mask materials under a range of flow velocities, which wasn’t studied before in that extent.
Found a hyperbolic relationship of permeability to the number of layers. Like I mentioned before, a parallel resistor type configuration.
We laid some groundwork to characterize deformation, but the theory of elastic fabric is complicated and will require further attention.

## Slide 39
Thank you
Questions ?

## Slide 41: How important is the inertial term?
Modified Darcy’s law:
The data are for a single layer material.
= 8 Pa*s/m
k’ = 2E-06 m
= 754 Pa*s/m
k’ = 2.43E-08 m
Notes: 2 sample, extreme cases

## Slide 42
Objectives
Identify the step-up/-down streamwise gust response.
Examine ability of a rotating & swept wingtip panel to mitigate gusts.
Lift force measurements, dye visualization, tomographic Particle Tracking Velocimetry (PTV)
Approach
Gust-ramp: accel./decel. rate.
Aspect ratio.
Actuation timing.
Parameters
Step-up gust
Step-down gust
U
U
U
Actuation-in
Actuation-out
U
Gust-CL behavior.
Gust-CL change from actuation.
Flow causing the force changes
Study
Rectangular plate with a swept rotating tip experiencing streamwise gust

## Slide 43
Force measurements
ATI Gamma sensor above wing.
1 kHz sampling; average 10 runs; subtract off results from air runs.
Low-pass filter to remove mechanical vibrations.
Experimental setup: force meas. & parameters
b
c
Λ
Umain
Upanel
𝛬
Parameters
Main-wing speed: Umain, Re O(104).
α = 45 panel sweep angle: Λ = 45.
AReff,rect = 2, 4 (Λ = 90); ARrect+panel = 4.1, 6 (Λ = 45).
Extended (Λ = 45) panel area: 31.7%, 15.8% of main wing.
Panel tip speed: Upanel = 1.5Umain, initial.
Re = 12k
Re = 18k
Re = 18k
Re = 9k
Time-avg. ±4%
±6.7%
CL
Chords traveled
Chords traveled
Step-up
Step-down

## Slide 44
Rectangular wing reference case: step-up/down
Step-up gusts
Step-down gusts
Spanwise outboard flow in LEV
End view
Top view

## Slide 45
AR = 4
AR = 2
Numerous shed LEVs
Actuation effects
Long time (without gust)
Starting flow
Actuation out
Actuation out
AR = 4
AR = 2

## Slide 46
*Not to scale
STB Experimental Setup
Tow direction
Water towing tank
4 cameras on a vibration isolation desk
Dual-head laser
Wing
Glass prisms
= 70 deg
Scheimpflug mounts
X
Z
Y

## Slide 47
*Not to scale
STB Experimental Setup
Dual-head laser
Wing
Tow direction
Water towing tank
X
Z
Y
High-speed laser head
Optics: 45 deg. mirror, volume optics,
f=-150mm & -90mm cylindrical lenses
Laser volume
Calibration target
Mechanical chopper
Fluorescent Polyethylene Microspheres
Density 1.00g/cc, diameter 100 micron

## Slide 48
PTV Operation
Programmable Timing Unit
Motion controller
Laser controller
Laser head

## Slide 49
dt: STB 6 ms (step-up), 15 ms (step-down) ; Eulerian data 65 ms (step-up), 75 ms (step-down).
Time-resolved measurement & processing details:

## Slide 50
dt: STB 6 ms (step-up), 15 ms (step-down) ; Eulerian data 65 ms (step-up), 75 ms (step-down).
Average raw signal-to-noise ratio: approximately 200:1.
Time-resolved measurement & processing details:
intensity

## Slide 51
dt: STB 6 ms (step-up), 15 ms (step-down) ; Eulerian data 65 ms (step-up), 75 ms (step-down).
Average raw signal-to-noise ratio: 200:1.
Perspective calibration using 3 planes (back, middle, and front of the volume).
Time-resolved measurement & processing details:
x
z
y

## Slide 52
dt: STB 6 ms (step-up), 15 ms (step-down) ; Eulerian data 65 ms (step-up), 75 ms (step-down).
Average raw signal-to-noise ratio: 200:1.
Perspective calibration using 3 planes (back, middle, and front of the volume).
Further correction using Volume Self-calibration; average disparity 0.05px.
Optical Transfer Function calculated.
Time-resolved measurement & processing details:

## Slide 53
dt: STB 6 ms (step-up), 15 ms (step-down) ; Eulerian data 65 ms (step-up), 75 ms (step-down).
Average raw signal-to-noise ratio: 200:1.
Perspective calibration using 3 planes (back, middle, and front of the volume).
Further correction using Volume Self-calibration; average disparity 0.05px.
Optical Transfer Function calculated.
STB uses Iterative Particle Reconstruction (IPR) for particle detection.
5 sets of STB data for each case merged.
VIC# converts Lagrangian field to Eulerian (spatial res: 2% chord/vector).
Time-resolved measurement & processing details:

## Slide 54
3 Eulerian fields per case with (25% overlap) stitched.
Velocity fields smoothed using a Gaussian filter.
Time-resolved measurement & processing details:

## Slide 55
1c: distance traveled of length 1 chord
Gust type | Gust accel./decel. dist. | Tip conditions tested
step-up | 1c | Rect., static sweep, actuation-in at 21.5c (50% gust dist.)
 | 3c | Rect., static sweep, actuation-in at 21.5c & 22.5c (50% dist.)
 | 6c | Rect., static sweep, actuation-in at 21.5c & 24.0c (50% dist.)
step-down | 1c | Rect., static sweep, actuation-out at 21.5c (50% dist.)
 | 3c | Rect., static sweep, actuation-out at 21.5c & 22.5c (50% dist.)
 | 6c | Rect., static sweep, actuation-out at 21.5c & 24.0c (50% dist.)
Rectangular
Static sweep
Actuation-in
Actuation-out

## Slide 56
Step-up gusts
Step-down gusts
Gust start
1c ends
3c ends
6c ends
Rectangular wing reference case: step-up/down
LEV
TV
TEV
shed LEV
TV
TEV
new LEV
End view
Top view
End view
Top view

## Slide 57
Rectangular wing reference case: step-up/down
Step-up gusts
Step-down gusts
Spanwise outboard flow in LEV
End view
Top view

## Slide 58
AR = 4
AR = 2
Numerous shed LEVs
Actuation effects
Long time (without gust)
Starting flow
Actuation out
Actuation out
AR = 4
AR = 2

## Slide 59
Step-up gust: tip actuation in
U
Static sweep
U
Rectangular

## Slide 60
Step-up gust: tip actuation in
1c ramp
3c ramp
6c ramp
AR=4
AR=2

## Slide 61
Total
circulation
98.4% span
S/c = 21.34
Merged 5 runs
Velocity smoothing
Using vorticity threshold
Phase-averaged 5 runs
No velocity smoothing
Zero vorticity threshold
Vorticity threshold

## Slide 62
Horseshoe vortex
wing
TEV
TV
LEV
S/c = 21.34
Using vorticity threshold
Zero vorticity threshold
Merged 5 runs
Velocity smoothing
Phase-averaged 5 runs
No velocity smoothing
Vorticity tensor
Strain-rate tensor
Q* = 4
isosurface
Q* = 4
isosurface
Merging vs Phase-averaging
Wing travel direction

## Slide 63
Total circulation for step-up gust
0.65b
0.75b
0.90b
1.05b
b = span
b
(Not to scale)
65% span
105% span
90% span
75% span

## Slide 64
Total circulation for step-up gust actuation-in case
0.65b
0.75b
0.90b
1.05b
b = span
b
1.15b
1.30b
(Not to scale)

## Slide 65
Step-down gust: tip actuation out
Static sweep
U
Rectangular
U

## Slide 66
Key points of the rotating wing model
Contributing factors to the model error:
The model is based on the assumption that rotating wing-flow creates a vortex loop comprised of LEV, TV, TEV and RV. A momentum balance gives the loop circulation.
This simplified loop-based approach may be useful for modeling other wing flows that produce coherent vortex loops.
Over-/under- prediction of loop circulation (Sullivan et al., JFM 2008)
Near-wake angle-of-attack scaling
Downwash calculation
Filtering of the experimental data and set-up constraints
Lift estimation with good accuracy.
Model’s only inputs: wing kinematics and geometry.
Notes: "The model is based on the assumption that rotating wing-flow creates a vortex loop consisting of the leading edge vortex, tip vortex, trailing edge vortex, and root vortex. A momentum balance gives the loop circulation." There are several factors that can contribute to the model’s deviation from the experiments or simulations. Sullivan et al. noticed in their piston problem that Γ can be over- or under- predicted up to 10% using momentum balance. A single loop angle theta is used to represent the orientation of the complex 3-D loop structure; this could incur some error, particularly the near-wake angle-of-attack scaling. Filtering of the experimental data, and set-up constraints such as mounting hardware are not captured by the model. But this simple physics based model does a great job, and needs only the wing kinematics and geometry as inputs. This model may be useful to model other wing flows that produce coherent vortex loops.

## Slide 67
Horseshow vortex
wing
TEV
TV
LEV

## Slide 69
Q-isosurface
Q=0.004 isosurface
LEV
TEV
TV
Vorticity tensor
Strain-rate tensor
Notes: The data acquisition is synchronized with the wing motion. ->
The motion controller operates the linear stage and when the wing reaches the entrance of the measurement domain,…it triggers the programmable timing unit, …which.. in turn, fires the laser and triggers the camera to capture multiple shots.

## Slide 70
Dual-head Nd:YLF Laser (527 nm) energy: 60 mJ per pulse when combined. (Photonics brand)
Pulse duration/width: 150 nanoseconds
Repetition rate: 1kHz full energy, 10kHz at low energy
We need frequency of 200Hz.
Phantom Vision Research Cameras (640L): CMOS
Frame rate: 1kHz at full resolution (4MP=2560*1600), 14kHz at 512*512
12 bit depth…meaning 4096 levels of intensity from pure black to white.
36 GB RAM onboard
Scheimpflug
LaVision DaVis software 10.1
Requires 10 particles in interrogation window
32px*32px*32px interrogation window a common take, and also at 50% overlap…computations are done on windows with size 32*32*32, but we get each vector in 16*16*16 due to 50% overlap…that means you get more vectors in your FOV…that means resolution is doubled.
PIV image processing:
t
t + Δt
image pair

## Slide 71
PIV Experimental Set-up
4 high-speed cameras
Tank
Glass prisms
Laser volume
Calibration target
High-speed laser head
Optics: 45 deg. mirror, volume optics, f=-150 & -90 cylindrical lenses
Mechanical chopper

## Slide 74
Prior work (variable wing geometry)
Wibawa et al. 2012, Steele et al. 2016: tested wings with various tip geometries mounted vertically in towing tank, suddenly retracted; studied shed vortices, energy release/recovery.
Wang et al. 2015: used CFD to examine dynamic changes in bat wing span. For increasing span, wing produces higher lift via stronger LEV.
van Oorschot et al. 2016: Static bird wings in translation, outboard sweep increases CL,max & stall angle.
Harvey et al. 2019: gulls use elbow joint to vary planform shape, a.c. vs. c.g., which may help with gust alleviation by changing pitching moment.
Scofield, Jia, Wei, & Bhattacharya 2019, Joshi, Vazquez, Kauffman, & Bhattacharya 2020: wing bending upward/downward, twisting to manipulate LEV, added-mass force peak.
Di Luca et al., Interface Focus, 2017
  Achieve 41% reduction in wing area.
  Expanded wing provides greater CL & maneuvering; retraction reduces CD for higher speed.
  Asymmetric actuation for roll control.

## Slide 76
Chords traveled during actuation
1c actuation out (step-down) | 0.34c
3c actuation out (step-down) | 0.5c
6c actuation out (step-down) | 0.5c
1c actuation in (step-up) | 0.79c
3c actuation in (step-up) | 0.57c
6c actuation in (step-up) | 0.54c
For actuations at 21.5 chords traveled.

## Slide 77
Planform view
b
c
Λ
Umain
Upanel
𝛬
Force measurements
ATI Gamma sensor above wing.
1 kHz sampling; average 10 runs; subtract off results from air runs.
Low-pass filter to remove mechanical vibrations.
Experimental setup: force meas. & parameters
Parameters
Main-wing speed: Umain, Re O(104).
α = 45 panel sweep angle: Λ = 45.
AReff,rect = 2, 4 (Λ = 90); ARrect+panel = 4.1, 6 (Λ = 45).
Extended (Λ = 45) panel area: 31.7%, 15.8% of main wing.
Panel tip speed: Upanel = 1.5Umain, initial.
Advance ratio: Jmax = Umaincos(α)cos(Λ)/Upanel = 0.5, should achieve attached panel-LEV (SEV) per J vs. AR results of Harbig et al., JFM 2014.
Re = 12k
Re = 18k
Re = 18k
Re = 9k
Precision error of mean CL (CL uses unsteady Umain & wing area)
Time-avg. ±4% (±0.05)
±6.7% (±0.08)
CL
Chords traveled
Chords traveled

## Slide 78
Starting flow: static-sweep has higher initial added-mass & circ. peaks than rect. (higher AR, SEV); earlier CL drop & earlier/higher 2nd circ. peak (SEV?).
Step-up gust, 1c: static-sweep vs. rect.—initial trends similar to starting flow.
Step-down gust: static-sweep and rect. very similar, except 1c deceleration—rect. has higher CL during initial recovery.
Static tip sweep vs. rectangular tip
Rectangular: AR = 4 Static-sweep: AR = 6
Step-down gusts
Step-up gusts

## Slide 79
Starting-flow: behavior consistent w/ AVT-202; CL collapses results for different Re.
CL using instantaneous Umain(t) makes starting & gust magnitudes comparable.
1c step-up force similar to 1c startup, consistent w/ Mulleners et al. (AIAAJ 2017).
Step-down case: small 1c recovery spike (Lift plot) could be continuation of circ. lift combined w/ added-mass effect, or just mechanical backlash.
Rectangular wing reference case: step-up/down
Dimensional lift (N)
CL using instantaneous Umain(t)
Gust start

## Slide 80
Experimental setup: uncertainty in force measurements
Static weight tests for 0.2−2 N give results within 1.5% of ATI calibration.
Compute precision error of mean using run-to-run variations: ; N = no. runs.
(Left plot) step-up actuation-in, time-average ±4% (±0.05); (right) step-down act.-out: ±6.7% (±0.08).
Re = 12k
Re = 18k
Re = 18k
Re = 9k
AR = 4, 1c step-up gust, actuation in
AR = 4, 1c step-down gust, actuation out
CL all cases uses instantaneous Umain(t) & time-varying wing area
Gamma transducer

## Slide 81
Comparison with fully-submerged wings
AR = 4
AR = 2

## Slide 82
Bio-inspired drones with sweep/area change
For MAV applications, see Li et al. “A review of modelling and analysis of morphing wings,” Prog. Aerosp Sci., 2018
RoboSwift: http://www.roboswift.nl/
NextGen MFX-1: Flanagan et al. AIAA Paper 2007-1707
Di Luca et al., Interface Focus, 2017
Achieve 41% reduction in wing area.
Expanded wing provides greater CL at low speed; retraction reduces CD for higher speed.
Asymmetric actuation for roll control.

## Slide 83
Prior work (sweep, rotation)
Approach here: combine tip sweep & rotation to affect vortex formation.
  Sweep promotes an LEV-TV connection in translating rectangular wings (Beem et al. '12) ; for a flapping wing in translation, sweep can enhance spanwise flow, aid in LEV attachment (e.g. Wong et al. '13, Wong & Rival ‘15).
  Wing rotation exhibits attached LEVs for low local Rossby no. (e.g. Lentink & Dickinson '09, Jardin & Colonius '18, Bhat et al. ‘19).
Prior studies on variable wing geometry:
  Wingtip bending/deflection upward/downward (e.g. Scofield et al. SciTech 2019, O’Donnell & Mohseni 2019).
  Dynamic changes in bat wing span (Wang et al. 2015) and Gulls’ planform shape (Harvey et al. 2019).
  For greater CL, wing expanding, and for lower CD , retraction (Di Luca et al. 2017).
Streamwise step-up gusts:
Starting & gust flow look similar (Mulleners et al. 2017). The flow is sensitive to the gust ramp for non-slender delta wings (Marzanek & Rival 2019).
Di Luca et al. 2017